## Slide 1: viiaPackage basics
Workshop – Day 1
Marijn Drillenburg, Jurriaan Floor, Carolina Fonseca and Reinier Ringers
June 28th, 2023
Internal use only

## Slide 2: Contents of the workshop
Setup viiaPackage
  Installation summary
  Templates within the workfolder
Modelling basics
  Gridlines
  Draft model
  Edit geometry
    Cavity walls
    Openings
    Lintels
    Shallow foundations
  How material info is stored
Loads
  Dead loads
  Imposed loads
Output files from modelscript
  Json
  Pictures
28 June 2023

## Slide 3: Set Up the VIIA Package
28 June 2023

## Slide 4: Installation summary
Workfolder
  Create a workfolder where the viiapackage will be installed. Note: the model files and the FEM assessments will be prepared and stored in this folder!
Installation of the viiapackage
  Download the setup files (protocol) and save them in the workfolder
  Run the setup files as admin  virtual env. with:
    VIIA package
    FEM-client for DataFusr
    All other requirements and packages
Packages are also installed in DIANA
Complete instructions can be found in the protocol
28 June 2023

## Slide 5: Scripts within the workfolder
Modelscript
Mainscript
Resultscript
User_config
To create the support conditions, base motions, load combinations and connections.
To create the analyses
To create and assign geometries, materials and non-seismic loads.
Creates result pictures, graphs, geo output, etc.
File with myviia credentials
28 June 2023

## Slide 6: Scripts within the workfolder
Modelscript
Mainscript
Resultscript
User_config
To create the support conditions, base motions, load combinations and connections.
To create the analyses
To create and assign geometries, materials and non-seismic loads.
Creates result pictures, graphs, geo output, etc.
File with myviia credentials
28 June 2023

## Slide 7: Starting with the Modelscript
The viiaPackage is imported
If needed the fem package and other functions can be imported
from viiapackage import *
Protocol
import rhdhv_fem
from rhdhv_fem import fem_math
28 June 2023

## Slide 8: Starting with the Modelscript
project = viia_create_project(project_name='1416T’, version_nr=1, object_part='Gehele object')
Create the project variable:
Versions
Existing situation  version_nr: 1, strengthening  version_nr > 1
analysis_type or reference_period can be changed but you will not be able to use the reporting functions.
Object part
Important! Compare analysis data to MYVIIA (analysis type, NPR version, etc.)
Inform the project leader to modify MYVIIA if required.
28 June 2023

## Slide 9: Setup environment – Exercise 1
Prepare an environment for this workshop.
Create folder for workshop
Install on DIANA.
  Select object ‘940M’
Test if viiaPackage was installed properly.
Protocol
MYVIIA
MYVIIA_SERVER_URL = 'https://viiadevbackend.azurewebsites.net'
Login name: workshopX@viiagroningen.nl
https://viiadevfrontend.z6.web.core.windows.net/index.html
28 June 2023

## Slide 10
28 June 2023

## Slide 11: Modelling Basics
28 June 2023

## Slide 12: Gridlines
Convert inspection data to structural schematisation
List unknowns and discuss with lead engineer
Protocol
28 June 2023

## Slide 13: Gridlines
28 June 2023
Determine grid and levels (better not adjust later)
Create the gridlines
Check your grid by plotting it (simple plots only for verification of input)
You can create as many grids as needed. Note that the first grid is the default!
x_grid = [0, 4.4, 6.7, 9.4, 12.1, 15.8, 17.9, 35.1] y_grid = [0, 1.3, 2.1, 3.7, 4.9, 8.1, 11.4, 16.4] grid = project.viia_create_orthogonal_grid([[x_grid, y_grid]], name='Main Grid')
grid.plot()
Protocol
# Create grid --> ground floor walls grid_bg = project.viia_create_orthogonal_grid([[0, 8.0, 11.75, 12.55, 15.50, 18.55, 21.90], [0, 4.80, 7.35, 8.45, 11.30]], name='Ground floor') # Create grid --> first floor walls grid_f1 = project.viia_create_orthogonal_grid([[0, 10.40, 15.50, 18.55], [0, 2.35, 7.35, 8.90, 11.30]], name='First floor') # Create grid --> second floor walls grid_f2 = project.viia_create_orthogonal_grid([[0, 3.60, 10.40, 14.50, 15.50], [0, 2.45, 8.80, 11.30]], name='Second floor') # Create grid --> roof grid_rafters = project.viia_create_orthogonal_grid([[2.15, 3.8, 6.1, 7.75, 8.9, 10, 11.2], [0, 2.45, 5.65, 8.80, 11.30]], name='Rafters')

## Slide 14: Draft model
Add walls per layer (<< B2 - B1 - N0 - N1 - N2 - N3 >>)  think of the layers as the phases in which the building would be constructed
Add floors & roofs  check spans (especially for elements with joist and planks)
Check by plotting
# Walls n0_wall_list = [ ['A1', 'B1', 'MW-KLEI<1945', 100], ['A2', 'B2', 'MW-KLEI<1945', 100], ['A1', 'A2', 'MW-KLEI<1945', 100], ['B1', 'B2', 'MW-KLEI<1945', 100]] project.viia_create_walls_on_grid(layer='N0', z_bottom=grid['L1'], z_top=grid['L2'], wall_list=n0_wall_list)
Protocol
# Floors n0_floor_list = [ ['A1', 'B1', 'B2', 'A2', 'LIN-HBV-PLANKEN-0.018-0.07-0.17-0.6’, 0]] project.viia_create_floors_on_grid(layer='N0', z_coordinate=grid['L1'], floor_list=n0_floor_list)
# Plot layer in 3D project.viia_plot_layers(layers='N0', view='3D')
28 June 2023

## Slide 15: Cavity walls
Cavity walls with/without wall ties
project.viia_create_cavity_wall_ties_from_list(['wall_1', 'wall_2', 'wall_3', 'wall_4'], cavity=0.1, wall_tie_distance=0.775)
This function implements:
viia_create_outer_leaf
viia_create_cavity_wall_ties
viia_connect_cavity_walls
viia_create_dummy_plate_between_walls
Protocol
docstring
28 June 2023

## Slide 16: Openings
Wall openings:
n0_wall_opening_list = [ ['wall_5', [[0.55, 2.45, 0, 2.5]]], ['wall_15', [[2.5, 0.65, 0.85, 1.15], [0.65, 0.65, 0.85, 1.15]]] ] project.viia_add_openings(opening_data_list=n0_wall_opening_list)
1. Distance from edge of wall to 1st opening OR distance from previous opening to the next
2. Width of the opening
3. Height from bottom of wall to opening
4. Height of the opening
1
1
2
3
4
28 June 2023

## Slide 17: Lintels
Auto generate lintels
project.viia_create_all_lintels(lintel_material='LIN-STAAL', lintel_type='HEA100', collection='N0')
Protocol
List of walls
‘All’ : all the walls in the model
Walls in a layer
28 June 2023

## Slide 18: Foundations
Concrete strip foundation
  Input: walls underneath which the foundation will be applied
  Foundation depth: Bottom side of the foundation, where the actual support is
project.viia_create_foundation_walls_and_strips( walls=walls_for_foundation, strip_material='LIN-MW-KLEI<1945', strip_width=600, strip_thickness=150, foundation_depth=grid['L1'])
Protocol
28 June 2023

## Slide 19: Foundations
Stepped foundation
  Input: walls underneath which the foundation will be applied.
  Foundation depth: Bottom side of the foundation, where the actual support is.
You can check the calculated properties with the excel sheet in rekentools (link)
project.viia_create_foundation_walls_and_strips( walls=walls_for_foundation, strip_material='LIN-MW-KLEI<1945', stepped_foundation_strip_extensions=[60, 75, 50], stepped_foundation_strip_heights=[120, 60, 80], foundation_depth=grid['L1'])
Nonlinear masonry
Linear masonry, real width, normal density
Linear masonry, equivalent thickness and density
Protocol
28 June 2023

## Slide 20: Interactive modelling
project.viia_start_interactive_modelling( level=levels[2], layer='N0', grid_lines=grid_main, geometry_material_combinations=[[100, 'MW-KLEI<1945'], [210, 'MW-KZS>1960']], shape_type='wall', top_level=levels[3] )
Demo video
28 June 2023

## Slide 21: How material info is stored
Refer for names of materials to UPR.
28 June 2023

## Slide 22: How material info is stored
Material model defines the structural model for the behaviour of the material.
Switch between linear and non-linear modelled material -> Replace the material model
You can get and set all attributes in python (be aware most parameters are VIIA defaults)
28 June 2023

## Slide 23: Exercise 2
Create basic model
  Create the grid
  Create the shapes: floors, walls, roofs
  Create some openings
  Create lintels
  Create the foundation
Create appendix C1 of the structure
Bonus:
Load in DIANA
28 June 2023

## Slide 24: Exercise 2
Stepped footing
Concrete strip
6.0 m
6.0 m
3.5 m
3.0 m
1.0 m
0.8 m
6.0 m
Walls: MW-KLEI<1945
Floors: LIN-HBV-PLANKEN-0.018-0.05-0.2-0.6
Roofs: LIN-HBV-PLATEN-0.018-0.05-0.2-0.6
28 June 2023

## Slide 25
28 June 2023

## Slide 26: Loads
28 June 2023

## Slide 27: Dead loads
Create self weight loadcase
Create resting loads
Protocol
# Loads on sloped roofs for roof in [roof_1, roof_2]: project.viia_create_surface_mass_floor(floor=roof, resting_load=['SlopeRoofLoad'])
project.viia_create_loads('Self weight')
Resting loads in viiaPackage
WindowLoad
FinishLoad
CeilingLoad
WallLoad
WallLoadLight
WallLoadMedium
WallLoadHeavy
InstalLoad
FlatRoofLoad
FlatRoofGravelLoad
SlopeRoofLoad
SlopeRoofLoadConcrete
SlopeRoofLoadClay
SunPanelLoad
Section 4.1.3 of the UPR
28 June 2023

## Slide 28: Dead loads
Create resting loads in openings
Applies opening load of 0.5 kN/m2 on openings in walls and roofs
Half the load will be applied on bottom and half on top of the opening
Applied as mass:
  Class III Beam 3D, 0.1m x 0.1m
  2.2m x 0.5 x 500 N/m2 / 9.1 m/s2 = 56.1 kg/m
  56.1 kg/m / 0.01m2 = 5610 kg/m3
Protocol
project.viia_create_mass_all_openings()
2.2m
28 June 2023

## Slide 29: Imposed loads
28 June 2023
Create imposed loads on floors
Imposed loads are created as load (reduction factors not applied yet)
Protocol
project.viia_create_loads(load='Imposed load', category='AFloor', connecting_shapes=project.collections.floors)
Imposed loads in the VIIA Package
'AFloor’
'AStairs’
‘ABalc’
'BOffice’
'CSchool’
'C1_2’
'C3_5’
'DShop’
'E’
‘F‘
’HRoof'

## Slide 30: Output files from modelscript
28 June 2023

## Slide 31: End of modelscript
# Connect all shapes project.viia_connect_all_shapes() # Set data properties to all shapes project.viia_create_all_datas() # View model in matplot project.viia_create_plots() # Create json-file from model (stored in model sub-folder) project.viia_write_dump() # Create pictures for building structural setup appendix project.viia_create_model_plots() # Create the building structural setup appendix project.viia_create_model_plots_appendix() # Create the PSSE NSCE plot project.viia_plot_psse_nsce()
Merges nodes in lines in the object to connect all shapes
Assigns the data properties to the shapes
Creates a 3D interactive view of the model
Creates the model json*  this file contains all the model information and is read later by the mainscript
Creates pictures of the structure and applied loads and materials
Creates the C3 appendix
Creates pictures with NSCEs and PSSEs
28 June 2023

## Slide 32: End of modelscript
28 June 2023

## Slide 33: Exercise 3
Create loads for residential usage
Create json-model
Bonus:
Apply load for the solar panels on part of the roof
UPR 9.0
28 June 2023