## Slide 1: viiaPackage basics
Workshop – Day 1
Marijn Drillenburg and Reinier Ringers
March 23rd & 30th 2022
Internal use only

## Slide 2: Contents of the workshop
Setup viiaPackage
  Python environments
  Modelscript vs mainscript
  The project variable
Python basics in viiaPackage
  Objects
Modelling basics
  Gridlines
  Draft model
  Edit geometry
    Cavity walls
    Lintels
    Shallow foundations
Loads
  Dead loads
  Imposed loads
  Overview
23 March 2022

## Slide 3: Setup viiaPackage
Protocol
Workfolder
  Virtual environment
viiaPackage
FEM-client for DataFusr
User config file
23 March 2022

## Slide 4: ModelScript start
Use the viiaPackage by importing it
Create the project variable
Compare analysis data to MYVIIA (analysis type, NPR version etc.)
Versions: Existing situation is version nr. 1, strengthening >1
You can change parameters analysis_type or reference_period, but you will not be able to use the reporting functions. Inform the projectleader to modify MYVIIA if required.
from viiapackage import *
project = viia_create_project(project_name='940M')
Protocol
23 March 2022

## Slide 5: ModelScript start
Scope with different objectparts
Specify the objectpart in input argument (use exact name)
project = viia_create_project(project_name='1084A', object_part='1 Woonhuis')
23 March 2022

## Slide 6: Live demo
23 March 2022

## Slide 7: Setup environment – Exercise 1
Prepare an environment for this workshop.
Create folder for workshop
Copy startup script to the workshop folder and run.
  Pause when asked for DIANA
  Select object ‘940M’
Test if viiaPackage was installed properly.
Protocol
MYVIIA
23 March 2022

## Slide 8: Modelling basics - Objects
Checkout how material info is stored.
Refer for names of materials to UPR.
23 March 2022

## Slide 9: Modelling basics - Objects
Material model defines the structural model for the behaviour of the material.
Switch between linear and non-linear modelled material -> Replace the material model
You can get and set all attributes in python (be aware most parameters are VIIA defaults)
23 March 2022

## Slide 10: Modelling basics – Exercise 2
Create concrete for VIIA analyses
  Create the material ‘BETON’
  Reduce the density to 2200 kg/m3
Create linear concrete
  Create the material
  Reduce the stiffness to 50%
Bonus:
Create a rectangular profile-geometry object (300x600, bxh) using the material object you have just created.
Create geometry of 0.1m for floor.
23 March 2022

## Slide 11
23 March 2022

## Slide 12: Modelling basics - Gridlines
Convert inspection data to structural schematisation
List unknowns and discuss with lead engineer
Protocol
23 March 2022

## Slide 13: Modelling basics - Gridlines
Determine grid and levels (better not adjust later)
Create the gridlines
Check your grid by plotting it (simple plots only for verification of input)
x_grid = [0, 4.4, 6.7, 9.4, 12.1, 15.8, 17.9, 35.1] y_grid = [0, 1.3, 2.1, 3.7, 4.9, 8.1, 11.4, 16.4] grid = project.viia_create_orthogonal_grid([[x_grid, y_grid]], name='Main Grid')
grid.plot()
Protocol
23 March 2022

## Slide 14: Modelling basics – Draft model
Add walls per layer (<< B2 - B1 - N0 - N1 - N2 - N3 >>)
Add floors, check spans (especially for timber floors with joist and planks)
Check by plotting
# Walls n0_wall_list = [ ['A1', 'B1', 'MW-KLEI<1945', 100], ['A2', 'B2', 'MW-KLEI<1945', 100], ['A1', 'A2', 'MW-KLEI<1945', 100], ['B1', 'B2', 'MW-KLEI<1945', 100]] project.viia_create_walls_on_grid(layer='N0', z_bottom=grid['L1'], z_top=grid['L2'], wall_list=n0_wall_list)
Protocol
# Floors n0_floor_list = [ ['A1', 'B1', 'B2', 'A2', 'LIN-HBV-PLANKEN-0.018-0.07-0.17-0.6', 188]] project.viia_create_floors_on_grid(layer='N0', z_coordinate=grid['L1'], floor_list=n0_floor_list)
# Plot layer in 3D project.viia_plot_layers(layers='N0', view='3D')
23 March 2022

## Slide 15: Modelling basics – Cavity walls
Cavity walls with/without wall ties
project.viia_create_cavity_wall_ties_from_list(['wall_1', 'wall_2', 'wall_3', 'wall_4'], cavity=0.1, wall_tie_distance=0.775)
This function implements:
viia_create_outer_leaf
viia_create_cavity_wall_ties
viia_connect_cavity_walls
viia_create_dummy_plate_between_walls
Protocol
23 March 2022
docstring

## Slide 16: Modelling basics – Openings & Lintels
Auto generate lintels
project.viia_create_all_lintels(lintel_material='LIN-STAAL', lintel_type='HEA100', collection='N0')
Protocol
23 March 2022

## Slide 17: Modelling basics – Foundations
Concrete strip foundation
  Input: walls underneath which the foundation will be applied
  Foundation depth: Bottom side of the foundation, where the actual support is
project.viia_create_foundation_walls_and_strips( walls=walls_for_foundation, strip_material='LIN-MW-KLEI<1945', strip_width=600, strip_thickness=150, foundation_depth=grid['L1'])
Protocol
23 March 2022

## Slide 18: Modelling basics – Foundations
Stepped foundation
  Input: walls underneath which the foundation will be applied.
  Foundation depth: Bottom side of the foundation, where the actual support is.
You can check the calculated properties with the excel sheet in rekentools (link)
project.viia_create_foundation_walls_and_strips( walls=walls_for_foundation, strip_material='LIN-MW-KLEI<1945', stepped_foundation_strip_extensions=[60, 75, 50], stepped_foundation_strip_heights=[120, 60, 80], foundation_depth=grid['L1'])
Nonlinear masonry
Linear masonry, real width, normal density
Linear masonry, equivalent thickness and density
Protocol
23 March 2022

## Slide 19: Modelling basics – Exercise 3
Create basic model
  Create the grid
  Create the shapes: floors, walls, roofs
  Create some openings
  Create lintels
  Create the foundation
Create appendix C1 of the structure
Bonus:
Load in DIANA / ABAQUS
23 March 2022

## Slide 20: Modelling basics – Exercise 3
Stepped footing
Concrete strip
6.0 m
6.0 m
3.5 m
3.0 m
1.0 m
0.8 m
6.0 m
Walls: MW-KLEI<1945
Floors: LIN-HBV-PLANKEN-0.018-0.05-0.2-0.6
Roofs: LIN-HBV-PLATEN-0.018-0.05-0.2-0.6
23 March 2022

## Slide 21
23 March 2022

## Slide 22: Loads – Dead loads
Create self weight loadcase
Create resting loads
Protocol
# Loads on sloped roofs for roof in [roof_1, roof_2]: project.viia_create_surface_mass_floor(floor=roof, resting_load=['SlopeRoofLoad'])
project.viia_create_loads('Self weight')
Resting loads in viiaPackage
WindowLoad
FinishLoad
CeilingLoad
WallLoad
WallLoadLight
WallLoadMedium
WallLoadHeavy
InstalLoad
FlattRoofLoad
SlopeRoofLoad
SlopeRoofLoadConcrete
SlopeRoofLoadClay
SunPanelLoad
23 March 2022

## Slide 23: Loads – Dead loads
Create resting loads in openings
Applies opening load of 0.5 kN/m2 on openings in walls and roofs
Half the load will be applied on bottom and half on top of the opening
Applied as mass:
  Class III Beam 3D, 0.1m x 0.1m
  2.2m x 0.5 x 500 N/m2 / 9.1 m/s2 = 56.1 kg/m
  56.1 kg/m / 0.01m2 = 5610 kg/m3
Protocol
project.viia_create_mass_all_openings()
2.2m
23 March 2022

## Slide 24: Loads – Imposed loads
Create imposed loads on floors
Imposed loads are created as load (reduction factors not applied yet)
Protocol
project.viia_create_loads(load='Imposed load', category='AFloor', connecting_shapes=project.collections.floors)
23 March 2022

## Slide 25: Modelling basics – Exercise 4
Create loads for residential usage
Create json-model
Bonus:
Apply load for the solar panels on part of the roof
23 March 2022

## Slide 26: Loads – Overview
Do not create loadcombinations in modelscript
Generate appendix C1, including loading schemas
Protocol
project.viia_create_appendix_c1_pictures()
project.viia_create_appendix_c1()
23 March 2022

## Slide 27: See you next week!
23 March 2022