## Slide 1: viiaPackage basics
Workshop - Day 2
Marijn Drillenburg and Reinier Ringers
March 23rd & 30th 2022
Internal use only

## Slide 2: Contents of the workshop – Day 2
Recap
Fixed base analyses
  Loads and supports
  Eigenvalue analysis
Servers
The VIIA team
  Automating team
  Technical masters
  Knowledge team
  Taskforces
Flexbase analyses
  Loads and supports
  Result handling: Geo-output
Strengthening measures
Reporting
  BSC
  TVA
  Appendices

## Slide 3: Recap
Modelscript
Generate json

## Slide 4: Fixed base analyses – Loading
Main script
Load the model
Convert imposed loads to self weight for fixed base analyses (A1-A4)
  Make sure to
Protocol
project = viia_create_project(project_name='XXXX', version_nr=1)
project.viia_read_dump('model/XXXX-model', False)
# Convert imposed loads to self weight (as extra density), imposed loads are created in modelscript project.viia_convert_imposed_loads_to_self_weight() # Create the load combination for dead load (static situation) project.viia_create_loadcombination_static()

## Slide 5: Fixed base analyses – Supports
Create fixed base supports (example for shallow foundations)
Provide numerical constraint for columns and beams
Protocol
# Add fixed base supports for shallow foundation (to fstrip collection) project.viia_create_supports('FixedBase’)
# Add boundary springs which prevent beams and columns from spinning project.viia_create_all_boundary_springs_for_static_analysis(spring_stiffness=50)

## Slide 6: Fixed base analyses – Linear materials
Convert to linear material properties
(and back)
Protocol
# For fixed base analysis set the materials (temporarily to linear) project.viia_linear_properties()
project.viia_non_linear_properties()

## Slide 7: Fixed base analyses – Static
Run static linear elastic analysis (A1)
  Select run = True to run directly in DIANA and handle results
Protocol
# Linear elastic static calculation (step A1 protocol) project.viia_analysis(analysis_nr='A1', run=True)
00:00:00 Out-file of A1 - Lineair statische analyse moved to analysis folder.
00:00:00 Result-file of A1 - Lineair statische analyse is locked, a copy is made in analysis folder.
00:00:00 The sum of the vertical loads is 829.3 kN.
00:00:00 The center of mass is x: 2.993 m and y: 6.021 m.
00:00:00 Runtime of A1: 24.5 s

## Slide 8: Fixed base analyses – Booleans mainscript
# Boolean to add boundary springs during static analysis boundary_spring_static = False # Analysis analysis = ['A1'] num_modes = 100 signal = ['S1'] run_analysis = True pictures = True # Boolean for mesh check mesh_check = True # Boolean for applying connections detailing = True # Boolean for report creation, set to True to create report report = False governing_analysis = 'S1' # Boolean for cost quantities cost_quantities = False
Analysis
Select analysis from A1, A2, A3, A4, A7, A10, A12, A13, A15.
Multiple inputs allowed.
Num_modes
Select the number of modes for A3 and/or A7.
Signal
Select analysis from S1, S2, S3, S4, S5, S6, S7, S8, S9, S10, S11.
Multiple inputs allowed.
Pictures
Create model pictures. This will be extended for result pictures, when you don’t want to generate result pictures when running analysis.
Cost_quantities
Generate and send cost key figures to cost engineer.

## Slide 9: Fixed base analyses – Exercise 5
Run the eigenfrequency analysis

## Slide 10: Fixed base analyses – LTH
Apply the base motions
factor * ags * importance_factor * nlth_factor
Importance factor (Consequence class in MYVIIA)
  CC1=1.0, CC2=1.1, CC3=1.2
NLTH factor 1.1 (7 signals)
ags (MYVIIA)
NEN cluster (MYVIIA)
9.8432532967 m/s2 * 0.1672g/1g * 1.1 * 1.1 = 1.9914 m/s2
project.viia_create_loads('Base motion') project.viia_add_basemotion_signals() project.viia_create_loadcombination_base_motion(‘S1')
Protocol

## Slide 11: VIIA Servers
Request access to Reinier or Jurriaan
  WPS will create SZ1 credentials
  We will provide access to the server
  Move files: \\NLRTMGHPAPS004\exchange
Policy
  Stick to folder naming
  Don’t use as external disk
  Close all applications when you leave
  Empty recycle bin
  Sign out
Protocol

## Slide 12
23 March 2022

## Slide 13: The VIIA team – Proposal
The process of an object
Objectparts
Scope
MRS/NLTH/REF
Size
Consequence class
Complexity
VIIA (MT)
Client NCG
Tender
Proposal
Budget

## Slide 14: The VIIA team – Object
The process of an object
Inspection
Desk study
Tender
Proposal
Inspection report

## Slide 15: The VIIA team – Object
The process of an object
Cost engineer
Engineering
Tender
Proposal
Geo
Editors

## Slide 16: The VIIA team – Engineering
The process of an object
Tender

## Slide 17: The VIIA team – Engineering
The process of an object
Tender

## Slide 18: The VIIA team – Engineering
The process of an object
Tender

## Slide 19: The VIIA team – Engineering
The process of an object
Tender

## Slide 20: The VIIA team – Engineering
The process of an object
Tender

## Slide 21: The VIIA team – Engineering
Team
Technical master
Tender
Task force

## Slide 22: The VIIA team – Engineering
Team
Technical master
Task force
Automating team
Tender
Knowledge team

## Slide 23: Reporting bugs / issue report
The issue report should provide:
name (without we cannot contact user and ask specifics),
scripts to reproduce the error (mainscript and model-json or modelscript) (if we can’t reproduce the error we will not be able to check if issue is solved),
clear description of the error encountered and why that is an error (sometimes we get remarks like the piles don’t work…),
clear description of the requirements of the solution (code-snippet if you solved the issue yourself),
environment: version of the fem-client and the version of the viiaPackage (including last date of updating the branch, or better the branch hash),
explanation of the attempts that have been undertaken to solve the issue.

## Slide 24: Flexbase analyses – Supports
# ===================================================================================================================== # Flexbase model supports (step 9 protocol) # ===================================================================================================================== # Create flexbase supports if any analysis is selected after A4 if any(a not in ['A1', 'A2', 'A3', 'A4'] for a in analysis) and project.version == 1: # Shallow foundation interface for flex base # Select for FexBaseGlobal or FlexBaseFinal (provide file from geo-technical adviser) # Delete this part if there is no shallow foundation in the model project.viia_create_supports(support_type='FlexBaseGlobal', material_file='USRDEF_940M_100%.dat') # Example FlexBaseFinal # project.viia_create_supports( # support_type='FlexBaseFinal', # additional_supported_shapes=['N0-VLOEREN-LIN-BETON-150-1'], # material_dictionary={ # 'USRDEF_XXXX_100%.dat': [fstrip for fstrip in project.collections.fstrips], # 'USRDEF_XXXX_100%_floor.dat': ['N0-VLOEREN-LIN-BETON-150-1']})
Creation of flexbase supports
Protocol
'MATERI' 1 NAME USRDEF_940M_100% DSNZ 4.15138E+08 DSSX 4.15138E+08 DSSY 4.15138E+08 RAYLEI 6.26231E-02 5.28754E-04 USRIFC COULOMB USRVAL 5.2100E-01 1.5000E+05 USRSTA 0.0 'END'

## Slide 25: Flexbase analyses – Supports
Combination of Fixed support and interface (shallow foundation)/spring (pile foundation)
Protocol

## Slide 26: Flexbase analyses – Loads
Eigenfrequency analysis (A7)
Non-linear static analysis (A10)
Protocol
Protocol
# Eigenvalue analysis flexbase (step A7 protocol) if 'A7' in analysis: project.viia_analysis(analysis_nr='A7', run=run_analysis, nmodes=num_modes)
# Nonlinear static flexbase analysis (step A10) if 'A10' in analysis: # Convert imposed loads to self weight (as extra density), imposed loads are created in modelscript project.viia_convert_self_weight_to_imposed_loads() project.viia_analysis(analysis_nr='A10', run=run_analysis) project.viia_convert_imposed_loads_to_self_weight() warnings.warn(f"Imposed Loads have been converted to self weight. If not running analysis directly " f"(i.e. 'run_analysis' is set to False), then analysis is incorrect. Close DIANA and open A10 from " f"{project.diana_settings.current_analysis_folder}")

## Slide 27: Flexbase analyses – Loads

## Slide 28: Flexbase analyses – NLS results
Result pictures
Geo Output
Protocol

## Slide 29: Flexbase analyses – Loads
Non-linear Time History analyses (A12)
In A12:
In A10:
Protocol
# Nonlinear time history flexbase analysis (step A12) if 'A12' in analysis: project.viia_create_loads('Base motion') project.viia_add_basemotion_signals() project.viia_create_loadcombination_base_motion(signal[0]) project.viia_create_datfile() project.viia_analysis(analysis_nr='A12', run=run_analysis, signals=signal)

## Slide 30: Flexbase analyses – Exercise 6
Create the A12 analysis for the workshop model in DIANA for signal S3.
Bonus:
Change the iteration method to ‘secant’ through the viiaPackage.

## Slide 31
23 March 2022

## Slide 32: Flexbase analyses - Result handling
Convergence graph
Base shear
Out-of-plane displacements
Result pictures
Acceleration graphs
Geo Output
Protocol

## Slide 33: Flexbase analyses - Result handling (2)

## Slide 34: Flexbase analyses - Result handling (3)

## Slide 35: Flexbase analyses - Result handling GeoOutput NLS
When running A10 analysis, set ‘run_analysis’ to True. geo_output_ nls is automatically created in analysis folder.
Alternatively, this can be manually created
Protocol

## Slide 36: Flexbase analyses - Result handling GeoOutput NLTH
Through the result script
Specify signal (str), geo_output (bool), bsc_nls_dir(Path) and tva_nls_dir (Path)
Protocol

## Slide 37: Flexbase analyses - Result handling GeoOutput

## Slide 38: Strengthening
Existing analyses shows deficiencies (BSC report)
Select measures -> maatregelen overleg
GMC
Cost engineer
Add measures in model and analyse
Update version number
Measures in MYVIIA
Protocol

## Slide 39: Strengthening – Result handling GeoOutput
No Strengthening - A10 for NLS and A12 for NLTH (version number: 1)
With Strengthening – A13 for NLS and A15 for NLTH (version number: 2)
In case strengthening is applied with no significant change in mass, specify tva_nls_dir same as bsc_nls_dir

## Slide 40: Reporting
BSC
  Beoordeling Seismische Capaciteit
TVA
  Technisch VersterkingsAdvies
Protocol

## Slide 41: Reporting
Requirements for viia_create_report() for NLTH
  General information is retrieved from MYVIIA
  Analyses folders (including images) for:
    A7 – Eigenvalue flex base
    A10 – NLS flex base
    A12 – NLTH flex base
  Manual replacement of images is possible -> partly work in progress
Protocol

## Slide 42: Thanks, we hope you enjoyed this workshop!